## Slide 1: High-Quality Vaccine Development Powered by Quality Control Using Automated Electrophoresis
Agilent Fragment Analyzer and TapeStation Systems

## Slide 2: Table of Content
    Importance of nucleic acid vaccine QC
    The advantage of automated electrophoresis
Nucleic acid sample QC introduction
Agilent Solutions
mRNA vaccine
DNA vaccine
    IVT RNA preparation workflow
      Screening of DNA Template
      Screening of the IVT RNA Product
      Addition of a PolyA Tail
      Quality Control Checks of Final Product
    DNA vaccine workflow
      Amplify and Isolate DNA of Interest
      Plasmid Purification
      Final Product
    Agilent Fragment Analyzer Systems
    Agilent TapeStation Systems
    Summary
    Resources

## Slide 3: Nucleic Acid Sample QC Introduction

## Slide 4: Importance of Nucleic Acid Vaccine QC
Utilizing sample QC checkpoints at critical junctures in the process identifies unsuitable samples, saves time and money, and thereby maximizing resources
Unsuitable samples may result from:
  Insufficient PCR amplification
  Suboptimal plasmid linearization
  Poor transcription
  DNA template contamination of RNA
  Degraded RNA
Sample QC ensures that downstream applications are starting with high-quality nucleic acids
Sample quality control (QC) analysis is an essential part of the in vitro transcription (IVT) RNA and DNA vaccine workflow.

## Slide 5: The Advantage of Automated Electrophoresis
An automated solution for nucleic acid analysis improves lab efficiency by:
  Faster time to results
  Objective, accurate and digital data
  Flexible throughput options
Automated
Manual
Agarose or acrylamide gels for DNA and RNA analysis are:
  Time-consuming
  Laborious
  Error-prone

## Slide 6: mRNA Vaccine
Workflow

## Slide 7: IVT RNA Preparation Workflow
QC step 1: DNA template
Synthetic DNA starting material can be made from linearized plasmids or PCR amplification.
QC step: Purity of PCR product and plasmid restriction digest screening
QC 1
Synthetic DNA starting materials
In vitro transcription
Addition of polyA tail
RNA cleanup
Formulation of RNA delivery system
Final product
QC 2
QC 3
QC 4
Process optimization
QC step 2: IVT RNA product
In vitro transcription (IVT) reactions need to be optimized to ensure the proper full product is produced with acceptable purity.
QC step: Qualitative and quantitative analysis of final product
QC step 3: Addition of a polyA tail
A polyA tail is added to the purified IVT product to increase stability.
QC step: Screening for tail length and quality to ensure degradation has not occurred
QC step 4: Final product
The final product is formulated and ready for shipment.
QC step: Screening for RNA stability and degradation
Notes: Blue arrows indicate that depending on the results of the QC checkpoint this step may have to be repeated.

## Slide 8: QC 1: Screening of DNA Template
QC 1
Synthetic DNA starting materials
In vitro transcription
Addition of polyA tail
RNA cleanup
Formulation of RNA delivery system
Final product
QC 2
QC 3
QC 4
Fragment Analyzer quantitative or qualitative kits can be used for fragment screening and plasmid restriction digest screening.
PCR product purity
Plasmid restriction
digest screening
Insert
Vector Backbone
Process optimization

## Slide 9: QC 2: Screening of the IVT RNA Product
1849 nt observed
1800 nt theoretical
The DNF-471 RNA Kit (15 nt) can be used for the assessment of the quality
and concentration of IVT RNA.
This analysis allows for the detection of incompletely transcribed RNA products enabling optimization of the IVT reaction.
QC 1
Synthetic DNA starting materials
In vitro transcription
Addition of polyA tail
RNA cleanup
Formulation of RNA delivery system
Final product
QC 2
QC 3
QC 4
Application note 5994-0512EN
Application note 5994-0878EN
Process optimization

## Slide 10: QC 3: Addition of a PolyA Tail
For Research Use Only. Not for use in diagnostic procedures. PR7000-8294
The addition of a polyA tail increases the half-life of the RNA once it has entered the targeted cells.
Electrophoretic QC allows for the monitoring of the approximate length of the polyA tail as well as monitoring for any degradation occurring.
DNF-471 or 472 RNA kits can be used to screen for addition of the polyA tail.
QC 1
Synthetic DNA starting materials
In vitro transcription
Addition of polyA tail
RNA cleanup
Formulation of RNA delivery system
Final product
QC 2
QC 3
QC 4
Process optimization

## Slide 11: QC 4: Quality Control Checks of Final Product
1849 nt observed
1800 nt theoretical
The DNF-471 RNA Kit (15 nt) can be used for the assessment of the quality
and concentration of IVT RNA up to 6000 nt without modification.
QC 1
Synthetic DNA starting materials
In vitro transcription
Addition of polyA tail
RNA cleanup
Final product
QC 2
QC 3
QC 4
Formulation of RNA delivery system
Process optimization

## Slide 12: QC 4: Quality Control Checks of Final Product
The amount of degradation can be determined using the ProSize data analysis software smear function.
Degraded IVT product
~70% of total
Desired product
QC 1
Synthetic DNA starting materials
In vitro transcription
Addition of polyA tail
RNA cleanup
Final product
QC 2
QC 3
QC 4
Formulation of RNA delivery system
Process optimization

## Slide 13: DNA Vaccine
Workflow

## Slide 14: DNA Vaccine Workflow
QC 1
Amplify and isolate DNA of interest
Ligate into plasmid
Purify plasmid
Transform into
bacteria
Formulate DNA
vaccine
Final product
QC 2
QC 3
For Research Use Only. Not for use in diagnostic procedures. PR7000-8294
QC step 1: Amplified DNA
Plasmid construction involves amplifying the target of interest and ligating this DNA sequence into the appropriate plasmid. The plasmid is transformed into a bacterial host that creates mass quantities of the plasmid of interest.
QC step: Screen PCR reactions for size and purity
QC step 2: Plasmid purification
Plasmid purified from the bacteria must be screened to ensure it contains the inserted DNA. Plasmid topology is also analyzed to quantitate the percent supercoiled.
QC step: Plasmid restriction digest product screening
QC step 3: Final product
After formulating the DNA plasmid into a delivery particle, the final product must be screened for the presence of the desired plasmid as well as topology.
QC step: Restriction digest, supercoiled plasmid sizing

## Slide 15: QC 1: Amplify and Isolate DNA of Interest
PCR product screening
For Research Use Only. Not for use in diagnostic procedures. PR7000-8294
Fragment Analyzer quantitative or qualitative kits can be used to screen PCR reactions for size and purity. These can be used to screen both the raw PCR reaction and after cleanup steps.
QC 1
Amplify and isolate DNA of interest
Ligate into plasmid
Purify plasmid
Transform into
bacteria
Formulate DNA
vaccine
Final product
QC 2
QC 3

## Slide 16: QC 2: Plasmid Purification
Plasmid restriction digest product screening
For Research Use Only. Not for use in diagnostic procedures. PR7000-8294
Fragment Analyzer qualitative kits can be used to screen plasmid restriction digests to identify plasmids containing the inserted sequence.
Plasmid topology cannot be measured at this time by the Fragment Analyzer.
Insert
Vector backbone
QC 1
Amplify and isolate DNA of interest
Ligate into plasmid
Purify plasmid
Transform into
bacteria
Formulate DNA
vaccine
Final product
QC 2
QC 3

## Slide 17: QC 2: Plasmid Purification
The Fragment Analyzer Plasmid kit can be used to screen supercoiled plasmids for size and purity of the purified plasmid. Plasmid topology cannot be measured at this time by the Fragment Analyzer.
Supercoiled plasmid sizing
For Research Use Only. Not for use in diagnostic procedures. PR7000-8294
QC 1
Amplify and isolate DNA of interest
Ligate into plasmid
Purify plasmid
Transform into
bacteria
Formulate DNA
vaccine
Final product
QC 2
QC 3
Application note 5994-4241EN

## Slide 18: QC 3: Final Product
Restriction digest, supercoiled plasmid sizing
For Research Use Only. Not for use in diagnostic procedures. PR7000-8294
The final DNA plasmid product undergoes quality control checks including sizing and restriction digests. These sample QC checks are the same as those completed during the construction of the plasmid (QC 2).
Amplify and isolate DNA of interest
Ligate into plasmid
Purify plasmid
Transform into
bacteria
Formulate DNA
vaccine
Final product
QC 3
QC 1
QC 2

## Slide 19: Agilent Solutions

## Slide 20: Agilent Fragment Analyzer Systems
Overview
For Research Use Only. Not for use in diagnostic procedures. PR7000-8294
3 benchtop models with different throughput options
Kits for RNA with specialized IVT RNA methods, DNA fragments, supercoiled plasmids, and NGS workflows
Qualitative and quantitative kits
6 array formats, customer choice for speed or resolution

## Slide 21: Agilent Fragment Analyzer Systems
Instrument models
For Research Use Only. Not for use in diagnostic procedures. PR7000-8294
Agilent 5200 Fragment Analyzer
    12 capillary array
    Sample trays for 3x96-well plates
    Agilent quality metrics
Agilent 5300 Fragment Analyzer
    48 capillary array
    96 capillary array
    Sample trays for 3x96-well plates
    Agilent quality metrics
Agilent 5400 Fragment Analyzer
Automated gel switching
    96 capillary array
    Interface with a robotic arm
    Operational software features
    APL commands
    LIMS capabilities
    Automated data analysis
    Agilent quality metrics

## Slide 22: Agilent Fragment Analyzer Systems
Unattended operation
Up to three 96-well plates,
or 288 samples, without
human intervention
Decreased platform preparation time
Room temperature stable reagents and no daily array handling
Method optimization
Change injection and electrophoresis conditions to optimize for unique sample needs
Low cost per sample Qualitative or quantitative gel kits that best suit your
analysis needs
Features & Benefits
Features and benefits
The Fragment Analyzer Systems utilize automated parallel capillary electrophoresis to provide reliable quality control for nucleic acids.
For Research Use Only. Not for use in diagnostic procedures. PR7000-8294
Application note 5994-0878EN

## Slide 23: Resources
Technical and application notes
Resolution of the Fragment Analyzers
Analysis of IVT RNA on the Fragment Analyzer Systems
Analysis of Long IVT RNA on the Fragment Analyzer Systems (method optimization)
Analysis of IVT sgRNAs on the Fragment Analyzer Systems
Analysis of IVT Cas9 mRNA
Plasmid Analysis Using the Agilent Fragment Analyzer Systems
White paper
Quality control steps for viral sequencing
Publications
BNT162b vaccines protect rhesus macaques from SARS-CoV-2
A single dose of self-transcribing and replicating RNA-based SARS-CoV-2 vaccine produces protective adaptive immunity in mice
A deletion in SARS-CoV-2 ORF7 identified in COVID-19 outbreak in Uruguay
A multiplexed, next generation sequencing platform for high-throughput detection of SARS-CoV-2

## Slide 24: Agilent Fragment Analyzer and TapeStation Systems
www.agilent.com/genomics/automated-electrophoresis